# VisualDOE 3.0 Two-Day Training Agenda

## Day One - 9:00 am (October 9, 2002)

| Introduction | Introductions Agenda/breaks Everyone up and running? Exercises Special requests? |
| --- | --- |
| Green Design Tools Overview | VisualPlant VisualRate VisualSch Other stuff on CD (DOE2.1E documentation) |
| Basic VisualDOE Concepts | Overview of VisualDOE Concept and History |
| Energy Simulation Introduction | Applications of Energy Simulation Introduction To DOE-2 Calculation Method (LSPE Modules) Capabilities and Limitations Sources of Information |
| Simulation Preview | Input Process Open a Sample Project Run Simulation Output View Results Introduction to VisualDOE Reports and Graphs View DOE2 files |
| Steps for Building Energy Simulation | Identify your objectives Thermal zoning plan Operation scheduling Internal loads Construction materials and assemblies Define space and zones Define HVAC systems and equipment Utility rates Keep it simple |

## Break

| Defining the Building Loads | Project Templates Selecting a Set of Units Inch-Pound SI (metric) Project Folder General Information Climate Utility Rates Economic Data Azimuth Holidays Custom Holidays Blocks What Is A Block? The Standard Block Shapes Rotating Block Shapes Adding Blocks Editing Concepts, Copying Pasting and Deleting Blocks Constructions Levels Floor Multipliers Zoning Patterns Plenum Setting/Applying Defaults Blocks Exercise 1 (w/o custom blocks) Introduction to Custom Blocks Creating and Editing Custom Blocks Using the Custom Block Editor Drawing New Rooms Entering and Editing Room Coordinates Blocks Exercise 2 (Introduction to custom blocks) |
| --- | --- |

## Lunch 12:00 -1:00 pm

| Defining the Building Loads (continued) | Rooms Rooms Equal Zones The Rooms List and Editing Concepts Properties Daylighting Group Editing Setting/Applying Defaults Rooms Exercise Facades The Facades List Typical Bay Method Assigning Construction Group Editing Setting/Applying Defaults Custom Facades Facades Exercise 3D Viewer |
| --- | --- |

## Break

| Mechanical Systems | Connecting Zones With Systems Single System for Whole Building System for Each Block System for Each Zone Custom Assignments HVAC System Editor Choosing a System Type Schedule Return Air Path Control Zone Setting and Applying Defaults System Features Equipment Templates Changing to Another System Type Defining Standard System Components Supply Fan Cooling System Heating System Defining Optional System Components Return Fan Humidifier Evaporative Pre-Cooling Heat Recovery Economizer Water Heating HVAC System Exercise Zone Level HVAC The Zones List and Editing Concepts Supply Air Outside Air Thermostats Exhaust Fans Zone Reheat and Baseboards PIU Properties Group Editing Setting/Applying Defaults Zone Exercise |
| --- | --- |

## Break

| Central Plant | Introduction To Central Plant Central Plant Editor Identifying the Plant Components The Concept of Templates Defining Chilled Water Plant Components Adding Chillers Selecting a Chiller Template Cooling Tower Pumps (Primary Secondary) Load Management Defining Hot Water Plant Components Boilers Pumps Load Management Central Plant Exercise Discussion What Did We Learn? Simplifying Assumptions |
| --- | --- |

### Wrap-up ~5:00 pm

## Day Two - 9:00 am (October 10, 2002)

| Defining Alternatives | Defining New Alternatives Changing Operating Hours Lighting Power Daylighting Skylights Glazing Type Construction Thermal Energy Storage |
| --- | --- |
| VisualDOE Organizers and Editors | Organizers and Editors Editing Openings Editing Glazings Editing Constructions (mass v. no mass) Editing Materials (incl. framing/insulation materials) Editing Occupancies Editing Schedules Editing Utility Rates |

## Break

|  | Schedule, Construction, and Utility Rate Exercises Rooms Skylights Daylighting Control Settings Open to Below Exterior Shading Misc. Energy Use Exterior Shade & Misc. Energy Exercise Thermal Energy Storage System |
| --- | --- |

## Lunch 12:00 - 1:00pm

| Evaluating Alternatives | Run ¦ Setup Choosing Design Alternatives to Run Choosing DOE-2 Reports to Create Hourly Reports Making the Run Creating Plant Load Profiles Diagnostics VisualDOE Results Reports and Graphs DOE-2 Reports Calibrating/Billing History Billing History Exercise Calibration Issues VisualDOE Reports Results Using Existing DOE-2 Files Editing DOE-2 Input Files Exporting Results |
| --- | --- |

## Break

| Advanced Inputs and Editing | DXF Import Multiple Meters Systems Special System Types and Components Evaporative Cooler Water Cooled Condenser Air-to-Air Heat Pump Water Source Heat Pump Natural Ventilation Central Plant Creating New Equipment Templates Absorb/Engine Chillers Cogeneration Climate Editor Sources of Weather Data Creating New Weather Files Updates, Technical Support, User Group |
| --- | --- |

### Wrap-up ~ 5:00 pm

# VisualDOE Training for LEED Energy Analysis

This training section is designed for VisualDOE users interested in performing LEED energy analysis. You will learn how to calculate energy savings versus ASHRAE Standard 90.1-1999/2001 for the purposes of LEED Energy Credit #1.

## Prerequisites

- Experience with VisualDOE 3.0 (2-day introductory training or equal)

- Knowledge of LEED rating systems, especially the Energy and Atmosphere Section (preferred)

- Basic knowledge of the ECB (Energy Cost Budget) Method of ASHRAE 90.1-1999/2001 (preferred)

- Laptop computer loaded with VisualDOE 3.0 and latest updates (via GDT Live Update), to participate in hands-on exercises. A limited number of computers may be available at the training site through prior arrangement.

## Scope of Training

- Overview of VisualDOE 3.0

- Overview of the LEED Green Building Rating System

- Overview of ECB Method – ASHRAE 90.1-1999/2001

- Creating the As-Built/Proposed Building Model

- Creating the ECB Alternative – LEED Baseline Building

- Running Simulations

- Creating the LEED Submittal Report

## Materials

- CD with presentation, VisualDOE templates and example files

- Certificate of VisualDOE training for LEED Energy Analysis

# Why Upgrade to VisualDOE 3.0

Users of earlier versions of VisualDOE will find an improved yet familiar interface, one that is widely praised for its ease-of-use relative to other simulation programs. However, VisualDOE 3.0 is a significant improvement over earlier versions with better performance and lots of new features.

## Benefits of Upgrading to VisualDOE 3.0

- Many critical and useful new features.

- Faster modeling and simulations.

- Easier simulation results diagnosis.

- Compatible with MS Windows 95/98/NT/ME/2000/XP.

- Periodic training seminars.

- Sharing VisualDOE 3.0 experience with users around the world in more than 35 countries.

## New Features

- Latest version of DOE-2.1E from Lawrence Berkeley National Laboratory. Increases the maximum number of zones from 128 to 1024 and systems from 128 to 256. Fixes bugs in earlier version of DOE-2.1E, and adds many new HVAC modeling features.

- Complete DOE-2.1E documentation in PDF format.

- Supports both IP and SI units.

- Skylight modeling capability.

- Improved editors for schedules, utility rates, and constructions .

- Ability to view and edit DOE-2 input and output files.

- Updated custom block editor for creating complicated building shapes.

- New façade editor for flexible window placement and use of multiple window types on each façade.

- Organizers to manage and reuse project and library items.

- Powerful 3D viewer.

- Increases in number of allowed design alternatives to 99.

- Project files contain schedule and construction data, independent of the library.

- Weather files included for several hundred USA and international locations.

- Automated updates via the Internet.

- And much more.

For upgrade pricing and further information please contact Eley Associates. Tel: (415)957-1977, email: support@eley.com, web: www.eley.com