Summary Comparison of Simulation Program Features

FEATURE

| Public/Proprietary | Public Domain | Proprietary | Proprietary | Proprietary |
| --- | --- | --- | --- | --- |
| Simulation Method | 8760 hours | 8760 hours | 8760 hours | 8760 hours |
| Loads Methodology | Cst Wtg Factor | Cst Wtg Factor | Std Wtg Factor | Std Wtg Factor |
| Load Design Calculation | No | No | Yes | Yes |
| Max # of Zones | 1024 | 1024 | Unlimited | 2500 |
| Front End Type | text/command | Windows | Windows | Windows |
| Multiple Interface Views |  |  | • |  |
| On-screen help | none | extensive | substantial | extensive |
| User-Selectable Hourly Output | extensive | extensive | limited | extensive |
| Graphic Results Summary |  | • |  | • |
| "3-D" Building Drawing |  | • |  |  |
| Accepts CAD input files/gbXML |  | • | • |  |
| Export Data back to CAD files |  |  | • |  |
| Materials/Assemblies Library | • | • | • | • |
| Schedules Library | • | • | • | • |
| Graphic Schedule Input |  | • |  | • |
| Bldgs/Prototype Library |  | • | • |  |
| Detailed Shading | • | • | • | • |
| Automatic Equip Sizing | limited | limited | • | • |
| Human Comfort Prediction |  |  |  |  |
| Expression Inputs | • | • |  |  |
| Multiple schemes / parametrics | • | • | • | • |
| # Terminal Systems Types | 28 | 28 | 24 | 21 |
| # Primary Equipment Types | 27 | 27 | 24 | 22 |
| Runtime (40 zones, 1.8MHz P4)* | 20 sec | 20 sec | 2.3 min | 2 min |
| Approximate Costc | freeware | freeware | $1995+$413/yr | $1495+$300/yr |
| Documentation | extensive | extensive | moderate | moderate |
| User modeling guide |  |  | included |  |
| Telephone and Email Help | not available | $450/10 hrs | extensive | limited |
| Minimum Hardware Recommended | Windows 9x+ 32 MB | Windows XP+ 32 MB | Windows XP+ 32 MB | Windows XP+ 32 MB |

* Dependent on tool version

Comparison of LOADS Modeling Capabilities

TRANE   CARRIER       	DOE2.2	eQUEST   TRACE       HAP

| Weather data |  |  |  |  |
| --- | --- | --- | --- | --- |
| Number of weather data days used | 365 | 365 | 12/365 | 365 |
| Statistical weather summaries available | • | • | • | limited |
| User-processing of custom weather data | • | • | • |  |
| Calculation Time Step |  |  |  |  |
| 1-hour in LOADS | • | • | • | • |
| 15 min or 30 min kW reporting | • | • |  |  |
| Spaces and Zones |  |  |  |  |
| Max # of Spaces / Zones | 1024 | 1024 | No max | 2500 |
| Spaces used as components of HVAC zones | • | • | • | • |
| Spaces/Zones named or numbered? | names | names | names | names |
| Floor and/or Space multipliers | • | • | • | • |
| Schedules |  |  |  |  |
| Maximum number of seasons per schedule | 52 | 52 | 12??? | 8 |
| Shading |  |  |  |  |
| Overhangs | • | • | • | • |
| Fins | • | • | • | • |
| Setbacks (I.e., "Reveals") | • | • | • | • |
| Detached (e.g., adjacent building) | • | • | • |  |
| Self-shading | • | • |  | limited |
| Shade transmittance schedulable | • | • | • |  |
| Operable interior/exterior shading | • | • | • | • |
| Glazing Systems Input Methods |  |  |  |  |
| Simple shading coefficient & conductance | • | • | • | • |
| Glazing library | • | • | • | • |
| User-definable layer-by-layer specification | • | • | •* | • |
| Lighting Systems Input Methods |  |  |  |  |
| Simple lighting power and/or density | • | • | • | • |
| Luminaire characteristics and Count | • | • |  |  |
| Desired illuminance (program calc's lighting power) | • | • | • |  |
| Max Number of Lighting & Equipment Loads per Zone | 5 | 5 | unlimited | 3 |
| Daylighting Levels Predicted on Request | • | • | • |  |
| Natural Ventilation | limited | limited | limited |  |

* Import from Windows 5 available

Comparison of Air-Side SYSTEM Modeling Capabilities

TRANE   CARRIER       	DOE2.2	eQUEST   TRACE       HAP

| Air-Side SYSTEMS Types |  |  |  |  |
| --- | --- | --- | --- | --- |
| Single Supply Duct Types |  |  |  |  |
| Packaged single-zone system | • | • | • | • |
| Single-zone fan system w optional sub-zone reheat | • | • | • | • |
| Constant volume reheat fan system | • | • | • | • |
| Single-zone inducion fan system | • | • | • | • |
| Variable volume (VAV) fan system, optional reheat | • | • | • | • |
| Fan-powered VAV (powered induction unit) system | • | • | • | • |
| Packaged variable volume system | • | • | • | • |
| Ceiling bypass variable volume system | • | • | • | • |
| Packaged variable volume / variable temperature | • | • | • | • |
| Packaged total gas solid desiccant system | • | • | • |  |
| Evaporative cooling system | • | • | • |  |
| Underfloor air distribution systems |  |  | • |  |
| Displacement ventilation systems |  |  | • |  |
| Active chilled beam system |  |  | • |  |
| Passive chilled beam system |  |  | • |  |
| Air Mixing Systems |  |  |  |  |
| Dual duct system | • | • | • | • |
| Dual fan dual duct system | • | • | • | • |
| Multizone system | • | • | • | • |
| Packaged multizone system | • | • | • | • |
| Terminal Unit Systems |  |  |  |  |
| Packaged terminal air conditioner | • | • | • | • |
| Unitary hydronic ("California") heat pump system | • | • | • | • |
| Two-pipe fan coil system | • | • | • | • |
| Four-pipe fan coil system | • | • | • | • |
| Two-pipe induction system | • | • | • | • |
| Four-pipe induction system | • | • | • | • |
| Variable refrigerant volume system |  |  | • |  |
| Ground-source heat pump system | • | • | • | • |
| Gas engine-driven heat pump system | • | • | • |  |
| Residential Systems |  |  |  |  |
| Packaged rooftop system | • | • | • | • |
| Split system | • | • | • | • |
| Variable volume / variable temperature system | • | • | • | • |
| Heating Only Systems |  |  |  |  |
| Heating and ventilating system | • | • | • | • |
| Unit heater | • | • | • |  |

Comparison of Air-Side SYSTEM Options

TRANE   CARRIER       	DOE2.2	eQUEST   TRACE       HAP

| Air-Side SYSTEMS Options |  |  |  |  |
| --- | --- | --- | --- | --- |
| Coil Sizing based on: |  |  |  |  |
| Coincident (building block) load | • | • | • | • |
| Non-coincident (sum of each zone) load | • | • | • | • |
| User-input | • | • | • | • |
| Thermostat Action Options |  |  |  |  |
| Two-position | • | • | • | • |
| Proportional | • | • | • | • |
| Reverse-acting | • | • | • | • |
| Automatic start-up cycles | • | • | • | • |
| Coil Control Options |  |  |  |  |
| Constant temperature | • | • | • | • |
| Reset by OSA | • | • | • | • |
| Reset by zone demand | • | • | • | • |
| User scheduled | • | • | • |  |
| Fan Control Options |  |  |  |  |
| Constant volume | • | • | • | • |
| Cycling | • | • | • | • |
| Two-speed | • | • | • |  |
| Inlet vane | • | • | • | • |
| Discharge dampers | • | • | • | • |
| Variable speed drives | • | • | • | • |
| User-definable curve | • | • | • | • |
| Fan static pressure optimization |  |  | • |  |
| Air-Side Economizer & Ventilation Options |  |  |  |  |
| Dry-bulb economizer | • | • | • | • |
| Enthalpy economizer | • | • | • | • |
| Fixed volume VAV control | • | • |  | • |
| Schedulable OSA quantities | • | • | • | • |
| Indirect and direct evaporative cooling |  |  | • |  |
| ASHRAE Standard 62.1 2004/2007 |  |  | • |  |
| Demand control ventilation |  |  | • |  |
| Adjacent room air transfer |  |  | • |  |
| Dedicated Outdoor Air Options |  |  |  |  |
| Split dehumidification |  |  | • |  |
| Dehumidification control |  |  | • |  |
| Control optimization (DB and Dew Point) |  |  | • |  |
| Active Dehumidification Controls |  |  |  |  |
| Worst case room |  |  | • |  |
| Mixed air bypass |  |  | • |  |
| Return air bypass |  |  | • |  |
| Variable speed fan |  |  | • |  |
| Heat Recovery Options |  |  |  |  |
| Multiple stages available |  |  | • |  |
| Heat pipe |  |  | • |  |
| Solid desiccant |  |  | • |  |
| Liquid desiccant |  |  | • |  |
| Type III desiccant |  |  | • |  |
| Sensible wheel |  |  | • |  |
| Total energy wheel |  |  | • |  |
| Coil runaround loops |  |  | • |  |
| Fixed plate heat exchanger |  |  | • |  |
| Fixed membrane heat exchanger |  |  | • |  |
| Duct losses |  |  |  |  |
| Direct, plenum, and ducted return paths | • | • | • | • |
| CFM loss reduces air to zone | • | • | • | • |
| Thermal & air losses affect surrounding zone temp | • | • | • |  |

Comparison of Water-Side PLANT Equipment Modeling Capabilities

TRANE   CARRIER       	DOE2.2	eQUEST   TRACE       HAP

| Water-Side PLANT Equipment Types |  |  |  |  |
| --- | --- | --- | --- | --- |
| Heating |  |  |  |  |
| Electric HW or steam boiler | • | • | • | • |
| Fuel HW or steam boiler | • | • | • | • |
| Cooling |  |  |  |  |
| 1-Stage & 2-stage HW or steam absorption chiller | • | • | • | • |
| Direct-fired 2-stage absorption chiller | • | • | • | • |
| Open/hermetic centrifugal chiller (water/air-cooled) | • | • | • | • |
| Open/hermetic reciprocating (water/air-cooled) | • | • | • | • |
| Rotary screw chiller (water/air-cooled) | • | • | • | • |
| Double bundle chiller | • | • | • |  |
| Engine-driven chiller | • | • | • | • |
| Central geothermal (cascaded or fully mixed) |  |  | • |  |
| Heat Rejection |  |  |  |  |
| Open cross-flow or counter-flow tower | • | • | • | • |
| Open cross-flow or counter-flow tower with HX | • | • | • | • |
| Ground loop | • | • | • |  |
| Scheduled temperature (e.g., lake, aquifer) | • | • | • | • |
| Evaporative precooling for DX systems | • | • | • |  |
| Chiller-tower optimization |  |  | • |  |
| Thermal Storage |  |  |  |  |
| Hot water storage | • | • | • |  |
| Chilled water storage | • | • | • |  |
| Ice or eutectic thermal storage | • | • | • |  |
| Electric Generating Equipment |  |  |  |  |
| Diesel engine | • | • | • |  |
| Photovoltaic Modules | • | • |  |  |
| Steam or gas turbine | • | • | • |  |
| Water-Side Economizer |  |  |  |  |
| Condenser water coils for DX systems | • | • | • |  |
| "Parallel" plate&frame or strainer cycle | • | • | • | • |
| "Series" plate&frame | • | • | • |  |
| Refrigerant migration |  |  | • |  |
| Fluid cooler |  |  | • |  |
| Load shedding |  |  | • |  |
| Other |  |  |  |  |
| Purchased steam or chilled water | • | • | • | • |
| Chilled water reset |  |  | • |  |
| Condenser water reset |  |  | • |  |
| Hot gas reheat for dehumidification |  |  | • |  |

Comparison of Water-Side PLANT Options

| Water-Side PLANT Equipment Options |  |  |  |  |
| --- | --- | --- | --- | --- |
| Plant Equipment Sizing based on: |  |  |  |  |
| User-defined design day weather | • | • | • | • |
| Annual weather file data | • | • | • |  |
| Heating and Cooling Equip Control Options |  |  |  |
| mixed equipment types | • | • | • | • |
| lead-lag equipment control | • | • | • | • |
| seasonal equipment control | • | • | • | • |
| time-of-day equipment control | • | • | • | • |
| preferential equipment loading | • | • | • |  |
| Cooling Tower Control Options |  |  |  |  |
| Fixed leaving water temperature | • | • | • | • |
| Wet-bulb reset | • | • | • | • |
| One-speed fans | • | • | • | • |
| Two-speed fans | • | • | • | • |
| Variable-speed fans | • | • | • | • |

# Text boxes

|  | TRANE | CARRIER |
| --- | --- | --- |
| DOE2.2 | eQUEST | TRACE 700 | HAP |

|  | TRANE | CARRIER |
| --- | --- | --- |
| DOE2.2 | eQUEST | TRACE | HAP |