T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  LDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- LV-B  SUMMARY OF SPACES OCCURRING IN THE PROJECT                                    WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

NUMBER OF SPACES    7          EXTERIOR    5     INTERIOR    2

LIGHTING              EQUIP

SPACE*FLOOR   SPACE           (WATT /            (WATT /  INFILTRATION  AIR CHANGES          AREA         VOLUME

SPACE        MULTIPLIER    TYPE  AZIMUTH   SQFT )   PEOPLE    SQFT )        METHOD     PER HOUR       (SQFT )        (CUFT )

N-1                20.0     EXT      0.0     2.00     28.0      1.00    AIR-CHANGE         0.90       2800.00       28000.00

E-2                20.0     EXT      0.0     2.00     28.0      1.00    AIR-CHANGE         0.90       2800.00       28000.00

S-3                20.0     EXT      0.0     2.00     28.0      1.00    AIR-CHANGE         0.90       2800.00       28000.00

W-4                20.0     EXT      0.0     2.00     28.0      1.00    AIR-CHANGE         0.90       2800.00       28000.00

I-5                20.0     INT      0.0     2.00     84.0      1.00    NO-INFILT.         0.00       8400.00       84000.00

C-6                20.0     INT      0.0     1.00      0.4      0.50    NO-INFILT.         0.00       3600.00       36000.00

PLEN               20.0     EXT      0.0     0.00      0.0      0.00    AIR-CHANGE         0.10      25600.00       89600.00

-------                                          ---------     ----------

BUILDING TOTALS                                     3927.2                                          976000.00     6432000.00

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  LDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- LS-A SPACE PEAK LOADS SUMMARY                                                       WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

MULTIPLIER   COOLING LOAD         TIME OF    DRY-  WET-    HEATING LOAD         TIME OF    DRY-  WET-

SPACE NAME         SPACE  FLOOR      (KBTU/HR)            PEAK    BULB  BULB       (KBTU/HR)            PEAK    BULB  BULB

N-1                  1.    20.          68.804    MAY 13  5 PM    88.F  72.F        -105.376    JAN 27  5 AM    -8.F  -9.F

E-2                  1.    20.         138.727    JUL  1 11 AM    94.F  75.F        -101.840    JAN 27  5 AM    -8.F  -9.F

S-3                  1.    20.         148.844    NOV  2  2 PM    67.F  53.F        -100.155    JAN 27  5 AM    -8.F  -9.F

W-4                  1.    20.         136.289    JUN  9  6 PM    95.F  72.F        -103.265    JAN 27  5 AM    -8.F  -9.F

I-5                  1.    20.         108.423    DEC 23  5 PM    19.F  17.F           0.000                     0.F   0.F

C-6                  1.    20.          14.694    DEC 23  7 PM    18.F  16.F           0.000                     0.F   0.F

PLEN                 1.    20.           0.000                     0.F   0.F        -124.465    JAN 26 12 MDNT  -3.F  -4.F

---------                                     ---------

SUM                                  12315.628                                    -10701.986

BUILDING PEAK                        10317.397    AUG 30  5 PM    94.F  76.F       -8212.688    JAN 27  5 AM    -8.F  -9.F

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  LDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- LS-D BUILDING MONTHLY LOADS SUMMARY                                                 WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

- - - - - - - - C O O L I N G - - - - - - - -      - - - - - - - - H E A T I N G - - - - - - - -      - - - E L E C - - -

MAXIMUM                                            MAXIMUM         ELEC-    MAXIMUM

COOLING     TIME   DRY-  WET-       COOLING        HEATING     TIME   DRY-  WET-       HEATING        TRICAL       ELEC

ENERGY   OF MAX   BULB  BULB          LOAD         ENERGY   OF MAX   BULB  BULB          LOAD        ENERGY       LOAD

MONTH     (MBTU)   DY  HR   TEMP  TEMP     (KBTU/HR)         (MBTU)   DY  HR   TEMP  TEMP     (KBTU/HR)         (KWH)       (KW)

JAN   1163.49841    7  15   35.F  30.F      4608.411      -2321.366   27   5   -8.F  -9.F     -8212.688       336866.   1177.000

FEB   1153.11084   25  16   45.F  38.F      6496.574      -1835.724    6   6    1.F   0.F     -6983.140       292548.   1177.000

MAR   1540.44592   18  16   62.F  46.F      8196.411      -1352.869    4   5   11.F   9.F     -5834.140       332280.   1177.000

APR   1967.52319   15  16   72.F  51.F      8896.806       -354.464   11   3   28.F  26.F     -3217.948       296183.   1177.000

MAY   2612.35034   12  16   90.F  74.F     10101.592       -102.188   16   5   39.F  37.F     -1997.118       288412.   1177.000

JUN   3330.55127    9  16   94.F  71.F      9836.854         -1.347   28   4   54.F  52.F      -276.730       289623.   1177.000

JUL   3619.05908    1  16   98.F  75.F      9873.542         -0.072   10   5   55.F  47.F       -42.191       268498.   1177.000

AUG   3623.91748   30  16   94.F  76.F     10317.397         -0.362   25   5   51.F  47.F      -172.758       307516.   1177.000

SEP   2974.75830   14  16   84.F  67.F      9724.140        -10.704   18   5   54.F  52.F      -575.617       293693.   1177.000

OCT   2207.05493    5  15   78.F  65.F      8950.961       -204.427   16   6   34.F  30.F     -2350.228       304488.   1177.000

NOV   1486.38367    2  15   68.F  54.F      8333.276       -757.081   28   5   19.F  17.F     -4334.380       314500.   1177.000

DEC   1145.35559   22  14   28.F  24.F      4051.136      -2173.563    2   6    6.F   4.F     -6496.356       343989.   1177.000

---------                          ----------      ---------                          ----------      --------    -------

TOTAL  26824.008                                          -9114.166                                          3668595.

MAX                                        10317.397                                          -8212.688                 1177.000

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  SDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- SV-A  SYSTEM DESIGN PARAMETERS                      AHU-1                           WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

FLOOR               OUTSIDE    COOLING               HEATING    COOLING    HEATING

SYSTEM   ALTITUDE       AREA        MAX        AIR   CAPACITY   SENSIBLE   CAPACITY        EIR        EIR

TYPE     FACTOR    (SQFT )     PEOPLE      RATIO  (KBTU/HR)      (SHR)  (KBTU/HR)  (BTU/BTU)  (BTU/BTU)

PIU           1.020   464000.0      3927.      0.120  29938.375      0.572 -16613.240      0.000      0.370

DIVERSITY    POWER       FAN     STATIC   TOTAL    MECH                         MAX FAN   MIN FAN

FAN   CAPACITY     FACTOR   DEMAND   DELTA-T   PRESSURE     EFF     EFF         FAN       FAN     RATIO     RATIO

TYPE    (CFM )     (FRAC)     (KW)       (F) (IN-WATER)  (FRAC)  (FRAC)   PLACEMENT   CONTROL    (FRAC)    (FRAC)

SUPPLY    670162.       1.00  795.633      3.75        6.5    0.63    0.72   DRAW-THRU     INLET      1.10      0.30

RETURN    670162.       1.00  242.883      1.14        2.0    0.64    0.71      RETURN     INLET      1.10      0.30

SUPPLY   EXHAUST             MINIMUM   OUTSIDE   COOLING          EXTRACTION   HEATING  ADDITION

ZONE             FLOW      FLOW       FAN      FLOW  AIR FLOW  CAPACITY  SENSIBLE      RATE  CAPACITY      RATE

NAME           (CFM )    (CFM )      (KW)    (FRAC)    (CFM ) (KBTU/HR)    (FRAC) (KBTU/HR) (KBTU/HR) (KBTU/HR) MULTIPLIER

PLEN                        0.        0.     0.000     0.000        0.      0.00      0.00      0.00      0.00      0.00       20.0

N-1                      3249.        0.     0.000     0.300      571.      0.00      0.00     68.80   -105.27    -49.54       20.0

E-2                      6551.        0.     0.000     0.300      571.      0.00      0.00    138.73   -212.25    -99.88       20.0

S-3                      7029.        0.     0.000     0.300      571.      0.00      0.00    148.84   -227.73   -107.17       20.0

W-4                      6436.        0.     0.000     0.300      571.      0.00      0.00    136.29   -208.52    -98.13       20.0

I-5                      5998.        0.     0.000     0.300     1714.      0.00      0.00    127.01   -194.32    -91.45       20.0

C-6                      2570.        0.     0.000     0.300        7.      0.00      0.00     54.43    -83.28    -39.19       20.0

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  SDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- SV-B  ZONE FAN DATA                     AHU-1                                       WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

FAN    SUPPLY       MIN    REHEAT       FAN

ZONE                  FLOW      FLOW      FLOW   DELTA-T   DELTA-T       FAN

NAME                (CFM )    (CFM )     RATIO       (F)       (F)        KW

PLEN                    0.        0.     0.000      85.0      0.00     0.000

N-1                     0.     3249.     0.300      85.0      0.00     0.000

E-2                     0.     6551.     0.300      85.0      0.00     0.000

S-3                     0.     7029.     0.300      85.0      0.00     0.000

W-4                     0.     6436.     0.300      85.0      0.00     0.000

I-5                     0.     5998.     0.300      85.0      0.00     0.000

C-6                     0.     2570.     0.300      85.0      0.00     0.000

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  SDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- SS-P  LOAD, ENERGY AND PART LOAD DHW TANK OPERATION FOR MAIN-PLANT                  WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

TANK SIZE is     350.0 ( GAL ) HEATER CAP =    286.096 (KBTU/HR) FLOW RATE =    10.000 (GAL/MIN    ) PUMP = ******* (KW)

UNIT LOAD  ENERGY USE  RCV EN USE  PUMP ENERGY    --------  Number of hours within each PART LOAD range  --------- TOTAL

SUM  (MBTU)      (MBTU)      (MBTU)      (KWH)          00    10    20    30    40    50    60    70    80    90   100   RUN

MONTH PEAK (KBTU/HR)   (KBTU/HR)    (KBTU/HR)    (KW)          10    20    30    40    50    60    70    80    90   100    +  HOURS

----- ---- ---------- ----------- ----------- -----------    ----  ----  ----  ----  ----  ----  ----  ----  ----  ----  ----  ----

JAN   SUM      45.658      76.760       0.000       0.000     379    67    57    52     0   105    21    21    21    21     0   744

PEAK    255.985     367.792       0.000       0.000

DAY/HR    31/13       31/13       31/24       31/24

FEB   SUM      42.744      71.696       0.000       0.000     347    58    50    46     0    57    38    38    19    19     0   672

PEAK    266.995     383.246       0.000       0.000

DAY/HR    28/13       28/13       28/24       28/24

MAR   SUM      51.718      85.441       0.000       0.000     359    23   101    54     0    69    46    23    46    23     0   744

PEAK    269.748     387.109       0.000       0.000

DAY/HR    31/13       31/13       31/24       31/24

APR   SUM      46.640      77.792       0.000       0.000     355    67    57    52     0    63    63    21    21    21     0   720

PEAK    261.490     375.519       0.000       0.000

DAY/HR    29/13       29/13       30/ 1       30/ 1

MAY   SUM      42.609      72.170       0.000       0.000     389    62    54    50    63    42    21    42    21     0     0   744

PEAK    242.223     348.475       0.000       0.000

DAY/HR    31/13       31/13       31/ 1       31/ 1

JUN   SUM      39.971      67.352       0.000       0.000     372    42    56    52    66    66    22    44     0     0     0   720

PEAK    217.450     313.708       0.000       0.000

DAY/HR    30/13       30/13       30/ 1       30/ 1

JUL   SUM      34.250      59.477       0.000       0.000     414    45   105     0   100    40    20    20     0     0     0   744

PEAK    200.935     290.532       0.000       0.000

DAY/HR    29/13       29/13       31/ 1       31/ 1

AUG   SUM      35.886      61.257       0.000       0.000     382   101    54    69    69    23    46     0     0     0     0   744

PEAK    187.172     271.220       0.000       0.000

DAY/HR    31/13       31/13       31/ 1       31/ 1

SEP   SUM      32.925      56.830       0.000       0.000     386    95    50    63    63    21    42     0     0     0     0   720

PEAK    187.172     271.220       0.000       0.000

DAY/HR    30/13       30/13       30/ 1       30/ 1

OCT   SUM      33.312      58.024       0.000       0.000     414    45   105    60    40    40    20    20     0     0     0   744

PEAK    195.430     282.807       0.000       0.000

DAY/HR    31/13       31/13       31/24       31/24

NOV   SUM      36.069      61.962       0.000       0.000     400    40   100     0    60    60    20    40     0     0     0   720

PEAK    214.697     309.846       0.000       0.000

DAY/HR    30/13       30/13       30/24       30/24

DEC   SUM      42.222      71.466       0.000       0.000     379    67    57    52    63    42    21    42    21     0     0   744

PEAK    236.718     340.749       0.000       0.000

DAY/HR    30/13       30/13       31/24       31/24

YR    SUM     484.002     820.263       0.000       0.000    4576   712   846   550   524   628   380   311   149    84     0  8760

PEAK    269.748     387.109       0.000       0.000

MON/DAY    3/31        3/31       12/31       12/31

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  SDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- SS-P  LOAD, ENERGY AND PART LOAD HW PUMP OPERATION FOR  MAIN-PLANT                  WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

PUMP SIZE is  2161.4 (GAL/MIN    )   HEAD =   60.0 (FT)   POWER =   35.26 (KW)   NUMBER = 1   MIN SPEED = 0.40

LOOP GAIN  ENERGY USE                             --------  Number of hours within each PART LOAD range  --------- TOTAL

SUM    (MBTU)    (KWH)                                  00    10    20    30    40    50    60    70    80    90   100   RUN

MONTH PEAK (KBTU/HR)     (KW)                                  10    20    30    40    50    60    70    80    90   100    +  HOURS

----- ---- ---------- ----------- ------------------------   ----  ----  ----  ----  ----  ----  ----  ----  ----  ----  ----  ----

JAN   SUM       0.000    9624.940                               0     0     0     0     0     0     0     0     0     0   273   273

PEAK                 35.256

DAY/HR                31/19

FEB   SUM       0.000    8708.288                               0     0     0     0     0     0     0     0     0     0   247   247

PEAK                 35.256

DAY/HR                28/19

MAR   SUM       0.000   10506.337                               0     0     0     0     0     0     0     0     0     0   298   298

PEAK                 35.256

DAY/HR                31/19

APR   SUM       0.000    9096.103                               0     0     0     0     0     0     0     0     0     0   258   258

PEAK                 35.256

DAY/HR                29/19

MAY   SUM       0.000    6980.734                               0     0     0     0     0     0     0     0     0     0   198   198

PEAK                 35.256

DAY/HR                31/19

JUN   SUM       0.000    1269.222                               0     0     0     0     0     0     0     0     0     0    36    36

PEAK                 35.256

DAY/HR                28/11

JUL   SUM       0.000     387.818                               0     0     0     0     0     0     0     0     0     0    11    11

PEAK                 35.256

DAY/HR                12/19

AUG   SUM       0.000     705.123                               0     0     0     0     0     0     0     0     0     0    20    20

PEAK                 35.256

DAY/HR                31/19

SEP   SUM       0.000    2961.518                               0     0     0     0     0     0     0     0     0     0    84    84

PEAK                 35.256

DAY/HR                30/19

OCT   SUM       0.000    6874.965                               0     0     0     0     0     0     0     0     0     0   195   195

PEAK                 35.256

DAY/HR                31/19

NOV   SUM       0.000    8884.567                               0     0     0     0     0     0     0     0     0     0   252   252

PEAK                 35.256

DAY/HR                30/19

DEC   SUM       0.000    9589.685                               0     0     0     0     0     0     0     0     0     0   272   272

PEAK                 35.256

DAY/HR                30/19

YR    SUM       0.000   75591.023                               0     0     0     0     0     0     0     0     0     0  2144  2144

PEAK                 35.256

MON/DAY               12/30

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  SDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- SS-P  LOAD, ENERGY AND PART LOAD CHW PUMP OPERATION FOR MAIN-PLANT                  WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

PUMP SIZE is  5982.9 (GAL/MIN    )   HEAD =   60.0 (FT)   POWER =   97.59 (KW)   NUMBER = 1   MIN SPEED = 0.40

LOOP GAIN  ENERGY USE                             --------  Number of hours within each PART LOAD range  --------- TOTAL

SUM    (MBTU)    (KWH)                                  00    10    20    30    40    50    60    70    80    90   100   RUN

MONTH PEAK (KBTU/HR)     (KW)                                  10    20    30    40    50    60    70    80    90   100    +  HOURS

----- ---- ---------- ----------- ------------------------   ----  ----  ----  ----  ----  ----  ----  ----  ----  ----  ----  ----

JAN   SUM       0.000     585.543                               0     0     0     0     0     0     0     0     0     0     6     6

PEAK                 97.591

DAY/HR                21/16

FEB   SUM       0.000    1268.677                               0     0     0     0     0     0     0     0     0     0    13    13

PEAK                 97.591

DAY/HR                25/18

MAR   SUM       0.000    5757.838                               0     0     0     0     0     0     0     0     0     0    59    59

PEAK                 97.591

DAY/HR                25/18

APR   SUM       0.000   18151.842                               0     0     0     0     0     0     0     0     0     0   186   186

PEAK                 97.591

DAY/HR                29/19

MAY   SUM       0.000   23909.643                               0     0     0     0     0     0     0     0     0     0   245   245

PEAK                 97.591

DAY/HR                31/19

JUN   SUM       0.000   27422.877                               0     0     0     0     0     0     0     0     0     0   281   281

PEAK                 97.591

DAY/HR                30/19

JUL   SUM       0.000   25373.490                               0     0     0     0     0     0     0     0     0     0   260   260

PEAK                 97.591

DAY/HR                29/19

AUG   SUM       0.000   28984.314                               0     0     0     0     0     0     0     0     0     0   297   297

PEAK                 97.591

DAY/HR                31/19

SEP   SUM       0.000   24885.541                               0     0     0     0     0     0     0     0     0     0   255   255

PEAK                 97.591

DAY/HR                30/19

OCT   SUM       0.000   21567.486                               0     0     0     0     0     0     0     0     0     0   221   221

PEAK                 97.591

DAY/HR                31/18

NOV   SUM       0.000   10637.367                               0     0     0     0     0     0     0     0     0     0   109   109

PEAK                 97.591

DAY/HR                30/14

DEC   SUM       0.000    1561.448                               0     0     0     0     0     0     0     0     0     0    16    16

PEAK                 97.591

DAY/HR                13/ 8

YR    SUM       0.000  190110.125                               0     0     0     0     0     0     0     0     0     0  1948  1948

PEAK                 97.591

MON/DAY               12/13

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  SDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- SS-A  SYSTEM MONTHLY LOADS SUMMARY FOR              AHU-1                           WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

- - - - - - - - C O O L I N G - - - - - - - -      - - - - - - - - H E A T I N G - - - - - - - -      - - - E L E C - - -

MAXIMUM                                            MAXIMUM         ELEC-    MAXIMUM

COOLING     TIME   DRY-  WET-       COOLING        HEATING     TIME   DRY-  WET-       HEATING        TRICAL       ELEC

ENERGY   OF MAX   BULB  BULB          LOAD         ENERGY   OF MAX   BULB  BULB          LOAD        ENERGY       LOAD

MONTH     (MBTU)   DY  HR   TEMP  TEMP     (KBTU/HR)         (MBTU)   DY  HR   TEMP  TEMP     (KBTU/HR)         (KWH)       (KW)

JAN      0.07768   20   7   19.F  16.F        27.559      -2388.943   31   8   18.F  15.F    -20689.992       457508.   1623.406

FEB      0.17777   22   8   32.F  29.F        32.588      -1836.119    1   8    4.F   3.F    -18140.195       401778.   1627.072

MAR     44.59280   25  10   64.F  59.F      5557.446      -1828.283   14   8   23.F  20.F    -15066.189       465461.   1640.401

APR    328.93027   25  14   77.F  63.F      9603.637      -1058.525   11   8   30.F  29.F     -9853.850       420741.   1636.625

MAY   1171.00879   12  17   90.F  74.F     15608.635       -566.472   16  13   53.F  40.F     -8684.911       419957.   1658.728

JUN   3089.66992    6   9   77.F  69.F     18987.945        -34.613   13   8   60.F  51.F     -6544.121       447143.   1710.554

JUL   3333.25513   18   9   81.F  74.F     20911.613         -5.564    5   7   62.F  54.F     -3166.433       419691.   1708.061

AUG   3618.48145   29  12   85.F  77.F     18819.225        -22.011   25  11   63.F  50.F     -3920.906       478180.   1778.741

SEP   2154.16431    6  12   79.F  71.F     16450.898       -124.894   28  13   64.F  49.F     -6064.480       436479.   1709.705

OCT    808.32526    7  17   77.F  65.F     11812.347       -456.572    3  19   53.F  41.F     -7283.673       426626.   1698.507

NOV    133.64146    3  15   73.F  58.F      7079.547      -1163.258   28   8   18.F  16.F    -13514.162       431267.   1655.499

DEC     19.63838    8   7   63.F  59.F      3987.114      -2097.221   27   8   15.F  14.F    -20570.447       464655.   1624.600

---------                          ----------      ---------                          ----------      --------    -------

TOTAL  14701.959                                         -11582.475                                          5269522.

MAX                                        20911.613                                         -20689.992                 1778.741

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- PV-A  EQUIPMENT SIZES                                                               WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

--------------  --------------  --------------  --------------  --------------  --------------

NUMBER          NUMBER          NUMBER          NUMBER          NUMBER          NUMBER

E Q U I P M E N T    SIZE  INSTD     SIZE  INSTD     SIZE  INSTD     SIZE  INSTD     SIZE  INSTD     SIZE  INSTD

(MBTU/H)  AVAIL (MBTU/H)  AVAIL (MBTU/H)  AVAIL (MBTU/H)  AVAIL (MBTU/H)  AVAIL (MBTU/H)  AVAIL

------------------  ------ -- --    ------ -- --    ------ -- --    ------ -- --    ------ -- --    ------ -- --

HW-BOILER           10.000  2  2

HERM-CENT-CHLR       7.000  2  2     7.000  1  1

COOLING-TWR         12.501  2  2

CTANK-STORAGE      250.113  1  1

COOL-STORE-RATE =      8.160 (MBTU/H)

COOL-SUPPLY-RATE=     12.000 (MBTU/H)

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- PS-A  PLANT ENERGY UTILIZATION SUMMARY                                              WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

*

S I T E   E N E R G Y                                            *  SOURCE

*

2        3        4        5        6        7        8        9        10       11       12       13   *    14

*

TOTAL    TOTAL    TOTAL             WASTED    FUEL     ELEC     FUEL     ELEC     FUEL    TOTAL    TOTAL  *  TOTAL

HEAT   COOLING   ELECTR   RCVRED  RCVRABL   INPUT    INPUT    INPUT    INPUT    INPUT     FUEL     SITE  *  SOURCE

LOAD     LOAD     LOAD    ENERGY   ENERGY  COOLING  COOLING  HEATING  HEATING   ELECT    INPUT    ENERGY *  ENERGY

MONTH   (MBTU)   (MBTU)   (MWH)    (MBTU)   (MBTU)   (MBTU)   (MWH)    (MBTU)   (MWH)    (MBTU)   (MBTU)   (MBTU) *  (MBTU)

-----  -------  -------  -------  -------  -------  -------  -------  -------  -------  -------  -------  ------- * -------

*

JAN    2359.4      1.9    542.3      0.0      0.0      0.0     15.3   3153.1     20.2      0.0   3153.1   5004.0 *  8927.6

*

FEB    1809.4      4.1    478.1      0.0      0.0      0.0     14.3   2463.3     16.9      0.0   2463.3   4095.1 *  7537.6

*

MAR    1796.0     62.3    563.6      0.0      0.0      0.0     20.8   2516.2     19.3      0.0   2516.2   4439.9 *  8478.1

*

APR    1030.8    600.7    550.4      0.0      0.0      0.0     49.0   1540.8     14.4      0.0   1540.8   3419.2 *  7313.9

*

MAY     545.3   1218.4    582.0      0.0      0.0      0.0     84.0    859.6      8.4      0.0    859.6   2845.8 *  6923.8

*

JUN      31.3   3061.9    699.0      0.0      0.0      0.0    182.4    114.8      0.6      0.0    114.8   2500.5 *  7350.1

*

JUL       4.4   3371.3    682.5      0.0      0.0      0.0    199.4     66.5      0.1      0.0     66.5   2395.8 *  7128.5

*

AUG      20.1   3713.4    769.0      0.0      0.0      0.0    218.8     93.0      0.5      0.0     93.0   2717.4 *  8050.7

*

SEP     116.0   2401.7    649.5      0.0      0.0      0.0    144.3    234.3      2.3      0.0    234.3   2451.2 *  6964.4

*

OCT     436.3    905.2    566.3      0.0      0.0      0.0     66.3    702.2      7.5      0.0    702.2   2635.0 *  6596.1

*

NOV    1136.1     44.8    531.1      0.0      0.0      0.0     28.6   1649.9     14.7      0.0   1649.9   3462.6 *  7229.7

*

DEC    2067.8     14.3    551.1      0.0      0.0      0.0     17.3   2792.4     18.9      0.0   2792.4   4673.1 *  8638.7

*

=======  =======  =======  =======  =======  =======  =======  =======  =======  =======  =======  ======= * =======

TOTAL  11352.9  15399.9   7164.8      0.0      0.0      0.0   1040.7  16186.1    123.7      0.0  16186.1  40639.5 * 91139.4

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- PS-B  MONTHLY UTILITY AND FUEL USE SUMMARY                                          WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

ELECTRICITY        NATURAL-GAS

METER-1            METER-1

MONTH                BTU/UNIT:       3413./KWH        100000./THERM

-------                            ----------------   ----------------

JAN

ENERGY CONSUMPTION (UNITS/MO)        542284.7            31531.3

PEAK DEMAND (UNITS/HR OR DAY)          2041.5              257.2

PEAK DAY/HR            7/17              31/ 8

FEB

ENERGY CONSUMPTION (UNITS/MO)        478089.7            24633.4

PEAK DEMAND (UNITS/HR OR DAY)          2090.5              230.4

PEAK DAY/HR           25/18               1/ 8

MAR

ENERGY CONSUMPTION (UNITS/MO)        563646.3            25161.7

PEAK DEMAND (UNITS/HR OR DAY)          2138.3              197.1

PEAK DAY/HR           25/ 9              14/ 8

APR

ENERGY CONSUMPTION (UNITS/MO)        550356.8            15408.0

PEAK DEMAND (UNITS/HR OR DAY)          2116.9              123.5

PEAK DAY/HR           15/19              11/ 8

MAY

ENERGY CONSUMPTION (UNITS/MO)        581971.4             8595.8

PEAK DEMAND (UNITS/HR OR DAY)          2548.0              113.4

PEAK DAY/HR           31/ 9              16/13

JUN

ENERGY CONSUMPTION (UNITS/MO)        698984.3             1148.4

PEAK DEMAND (UNITS/HR OR DAY)          2677.4               87.4

PEAK DAY/HR            6/ 9              13/ 8

JUL

ENERGY CONSUMPTION (UNITS/MO)        682483.3              665.0

PEAK DEMAND (UNITS/HR OR DAY)          2719.7               47.7

PEAK DAY/HR           18/ 9               5/ 7

AUG

ENERGY CONSUMPTION (UNITS/MO)        768953.6              929.9

PEAK DEMAND (UNITS/HR OR DAY)          2866.5               58.2

PEAK DAY/HR           29/ 9              25/11

SEP

ENERGY CONSUMPTION (UNITS/MO)        649539.6             2343.0

PEAK DEMAND (UNITS/HR OR DAY)          2658.7               83.7

PEAK DAY/HR           15/18              28/13

OCT

ENERGY CONSUMPTION (UNITS/MO)        566307.8             7021.9

PEAK DEMAND (UNITS/HR OR DAY)          2419.2               95.8

PEAK DAY/HR            7/19               3/13

NOV

ENERGY CONSUMPTION (UNITS/MO)        531117.2            16498.7

PEAK DEMAND (UNITS/HR OR DAY)          2194.5              179.7

PEAK DAY/HR            1/18              28/ 8

DEC

ENERGY CONSUMPTION (UNITS/MO)        551063.2            27923.6

PEAK DEMAND (UNITS/HR OR DAY)          2180.6              255.9

PEAK DAY/HR            8/18              27/ 8

-------                            ----------------   ----------------

TOTAL

ENERGY CONSUMPTION (UNITS/YR)       7164798.0           161860.8

PEAK DEMAND (UNITS/HR OR DAY)          2866.5              257.2

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- PS-C  EQUIPMENT PART LOAD OPERATION                                                 WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

TOTAL   ANNUAL    FALSE    ELEC    THERMAL

HOURS AT PERCENT PART LOAD RATIO                    HOURS    LOAD     LOAD     USED     USED

EQUIPMENT                                                                                   (MBTU)   (MBTU)   (KWH)    (MBTU)

0 -- 10 -- 20 -- 30 -- 40 -- 50 -- 60 -- 70 -- 80 -- 90 -- 100 - 110+ -----   ------   ------   ------   ------

HW-BOILER        227   182   126   141   244   321   342   233   111    75    99     2101   11353.0      0.0  123681.  15365.8

409   267   565   505   172    96    49    21    12     2     3

HERM-CENT-CHLR   180   102    84    68    40   172    97    92    89   257  1051     2232   15350.6      0.0  750580.      0.0

366   134    50  1263   121   107   191     0     0     0     0

COOLING-TWR      451   116    77   610   405   300   194   106    30    23     0     2312   18241.9      0.0  114902.      0.0

562   680   621   223    74    62    56    29     5     0     0

CTANK-STORAGE    206    72    48    40     8    37    56    85    96    71   346     1065    8356.2      0.0   21300.      0.0

1065     0     0     0     0     0     0     0     0     0     0

HOT  LOOP CIRCULATION PUMP ELECTRICAL USE =       0. KWH

COLD LOOP CIRCULATION PUMP ELECTRICAL USE =       0. KWH

CONDENSER    WATER    PUMP ELECTRICAL USE =   86692. KWH

TOWER  OR  CONDENSER  FAN  ELECTRICAL USE =   28210. KWH

NOTES TO TABLE

1) THE FIRST PART LOAD ENTRY FOR EACH PIECE OF EQUIPMENT IS

THE HOURLY LOAD DIVIDED BY THE HOURLY OPERATING CAPACITY

2) THE SECOND PART LOAD ENTRY FOR EACH PIECE OF EQUIPMENT IS

THE HOURLY LOAD DIVIDED BY THE TOTAL INSTALLED CAPACITY

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- PS-H  EQUIPMENT USE STATISTICS                                                      WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

--------

AVG     MAX   MON        ------------  ------------  ------------  ------------  ------------

E Q U I P M E N T    OPER   LOAD      DAY     SIZE  OPER    SIZE  OPER    SIZE  OPER    SIZE  OPER    SIZE  OPER

RATIO  (MBTU)        HR   (MBTU)  HRS   (MBTU)  HRS   (MBTU)  HRS   (MBTU)  HRS   (MBTU)  HRS

------------------  -----  ------  -- -- --   ------ -----  ------ -----  ------ -----  ------ -----  ------ -----

HW-BOILER           0.519  20.582   1 31  8   10.000  2188

HERM-CENT-CHLR      0.784  14.423   6  7 19    7.000  1661   7.000  1136

COOLING-TWR         0.565  16.967   6  7 19   12.501  2581

CTANK-STORAGE       0.665  14.400   9  6 17  250.113  1065

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- PS-D  PLANT LOADS SATISFIED                                                         WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

HEATING LOADS                 MBTU SUPPLIED      PCT OF TOTAL LOAD

-------------------------     -------------      -----------------

HW-BOILER                      11353.0             100.0

=============      =================

LOAD SATISFIED           11353.0             100.0

TOTAL LOAD ON PLANT           11353.0

COOLING LOADS                 MBTU SUPPLIED      PCT OF TOTAL LOAD

-------------------------     -------------      -----------------

HERM-CENT-CHLR                 15350.6              99.7

COOLING-TWR                        0.0               0.0

=============      =================

LOAD SATISFIED           15350.6              99.7

TOTAL LOAD ON PLANT           15399.9

ELECTRICAL LOADS              KWH SUPPLIED       PCT OF TOTAL LOAD

-------------------------     -------------      -----------------

ELECTRICITY                  7164798.0             100.0

=============      =================

LOAD SATISFIED         7164798.0             100.0

TOTAL LOAD ON PLANT         7164878.5

STORAGE TANK USE              MBTU STORED   MBTU RETURNED   MBTU LOST   MBTU RESIDUAL

-------------------------     -----------   -------------   ---------   -------------

CTANK-STORAGE                 8470.2          8356.2        0.00          113.96

TOWER ABOVE DESIGN TEMPERATURE OF 85.F   0 HOURS

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- PS-D  PLANT LOADS SATISFIED                                                         WEATHER FILE- CHICAGO, IL

--------------------------------------------------------------------------------------------------------------(CONTINUED)--------

SUMMARY OF LOADS MET

TOTAL       LOAD        TOTAL       PEAK        HOURS

TYPE OF LOAD          LOAD      SATISFIED   OVERLOAD    OVERLOAD   OVERLOADED

(MBTU)      (MBTU)      (MBTU)      (MBTU)

--------------------  ----------  ----------  ----------  ----------  ----------

HEATING LOADS            11353.0     11353.0       0.000       0.000        0

COOLING LOADS            15399.9     15350.6     214.585       6.885      128

ELECTRICAL LOADS         24453.5     24453.2       0.000       0.000        0

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- BEPS  BUILDING ENERGY PERFORMANCE SUMMARY                                           WEATHER FILE- CHICAGO, IL

---------------------------------------------------------------------------------------------------------------------------------

ENERGY TYPE:   ELECTRICITY   NATURAL-GAS

UNITS: MBTU

CATEGORY OF USE

---------------

AREA LIGHTS        7760.3           0.0

MISC EQUIPMT        4760.4           0.0

SPACE HEAT         422.1       15365.8

SPACE COOL        2561.7           0.0

HEAT REJECT         392.2           0.0

PUMPS & MISC        1504.8           0.0

VENT FANS        5463.7           0.0

DOMHOT WATER           0.0         820.3

EXT MISC        1587.9           0.0

----------    ----------

TOTAL       24453.1       16186.1

TOTAL SITE ENERGY     40639.17 MBTU     87.6 KBTU/SQFT-YR GROSS-AREA     87.6 KBTU/SQFT-YR NET-AREA

TOTAL SOURCE ENERGY   91138.20 MBTU    196.4 KBTU/SQFT-YR GROSS-AREA    196.4 KBTU/SQFT-YR NET-AREA

PERCENT OF HOURS ANY SYSTEM ZONE OUTSIDE OF THROTTLING RANGE =  4.8

PERCENT OF HOURS ANY PLANT LOAD NOT SATISFIED                =  1.5

NOTE:  ENERGY IS APPORTIONED HOURLY TO ALL END-USE CATEGORIES.

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  EDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- ES-D  ENERGY COST SUMMARY

----------------------------------------------------------------------------------------------------------------------------------

METERED              TOTAL       VIRTUAL

ENERGY             CHARGE          RATE    RATE USED

UTILITY-RATE        RESOURCE            METERS               UNITS/YR               ($)       ($/UNIT)    ALL YEAR?

----------------    ----------------    -----------    -------------------    ----------    ----------    ---------

ELEC-ENERGY         ELECTRICITY          1 2 3 4 5       7164798. KWH            890029.        0.1242       YES

GAS-ENERGY          NATURAL-GAS          1 2 3 4 5        161861. THERM           67699.        0.4183       YES

==========

957728.

ENERGY COST/GROSS BLDG AREA:      2.06

ENERGY COST/NET BLDG AREA:      2.06

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

PLANT-HOUR-REP   = HOURLY-REPORT                                                                                     PAGE  2 -  1

---------------------------------------------------------------------------------------------------------------------------------

HERM-CEN       HERM-CEN      HERM-CEN    HERM-CEN    HERM-CEN     HERM-CEN     HERM-CEN     HERM-CEN   HERM-CEN

T-CHLR         T-CHLR        T-CHLR      T-CHLR      T-CHLR       T-CHLR       T-CHLR       T-CHLR     T-CHLR

LOAD           ELECTRIC      TOWER       SIZES       NOM CAP      AVAL CAP     AVAL         OPER PT    FRAC HR

USE           LOAD        RUNNING     RUNNING      RATIO        CAPACITY     LD RATIO   OPERATED

BTU/HR         KW            BTU/HR                  BTU/HR       FRAC.OR      BTU/HR       FRAC.OR    FRAC.OR

MULT.                     MULT.      MULT.

----( 1)       ----( 3)      ----( 5)    ----( 6)    ----( 7)     ----( 8)     ----( 9)     ----(10)   ----(11)

7 1 1       7196652.       349.786       8390463.      10.       7000000.      1.028       7196652.      1.000      1.000

7 1 2       7196650.       349.787       8390462.      10.       7000000.      1.028       7196650.      1.000      1.000

7 1 3       7200480.       349.129       8392047.      10.       7000000.      1.029       7200480.      1.000      1.000

7 1 4       7200477.       349.130       8392046.      10.       7000000.      1.029       7200477.      1.000      1.000

7 1 5       7201966.       348.865       8392630.      10.       7000000.      1.029       7201966.      1.000      1.000

7 1 6       7200475.       349.130       8392045.      10.       7000000.      1.029       7200475.      1.000      1.000

7 1 7      12582378.       594.012      14609723.       2.      14000000.      1.029      14400954.      0.874      1.000

7 1 8      14345332.       706.612      16756978.       2.      14000000.      1.025      14345332.      1.000      1.000

7 1 9      14305045.       711.438      16733160.       2.      14000000.      1.022      14305045.      1.000      1.000

7 110      14291764.       712.876      16724788.       2.      14000000.      1.021      14291764.      1.000      1.000

7 111       7158658.       353.739       8365959.       2.      14000000.      1.021      14291816.      0.501      1.000

7 112       1514007.       109.422       1887461.       1.       7000000.      1.025       7172701.      0.211      1.000

7 113       2018060.       120.827       2430438.       1.       7000000.      1.029       7205760.      0.280      1.000

7 114       2268515.       128.096       2705703.       1.       7000000.      1.029       7203988.      0.315      1.000

7 115       2453427.       133.693       2909719.       1.       7000000.      1.029       7203058.      0.341      1.000

7 116       2477657.       134.490       2936666.       1.       7000000.      1.029       7202360.      0.344      1.000

7 117       1907744.       118.054       2310660.       1.       7000000.      1.029       7202267.      0.265      1.000

7 118      14408771.       696.843      16787074.       2.      14000000.      1.029      14408771.      1.000      1.000

7 119             0.         0.000             0.       0.             0.      0.000             0.      0.000      0.000

7 120             0.         0.000             0.       0.             0.      0.000             0.      0.000      0.000

7 121             0.         0.000             0.       0.             0.      0.000             0.      0.000      0.000

7 122             0.         0.000             0.       0.             0.      0.000             0.      0.000      0.000

7 123             0.         0.000             0.       0.             0.      0.000             0.      0.000      0.000

7 124       7158198.       355.077       8370065.      10.       7000000.      1.023       7158198.      1.000      1.000

DAILY SUMMARY (JUL  1)

MN             0.         0.000             0.       0.             0.      0.000             0.      0.000      0.000

MX      14408771.       712.876      16787074.      10.      14000000.      1.029      14408771.      1.000      1.000

SM     140086256.      6971.005     163878080.      88.     175000000.     19.510     179588720.     14.130     19.000

AV       5836928.       290.459       6828254.       4.       7291666.      0.813       7482864.      0.589      0.792

MONTHLY SUMMARY (JUL)

MN             0.         0.000             0.       0.             0.      0.000             0.      0.000      0.000

MX      14408771.       712.876      16787074.      10.      14000000.      1.029      14408771.      1.000      1.000

SM     140086256.      6971.005     163878080.      88.     175000000.     19.510     179588720.     14.130     19.000

AV       5836928.       290.459       6828254.       4.       7291666.      0.813       7482864.      0.589      0.792

YEARLY SUMMARY

MN             0.         0.000             0.       0.             0.      0.000             0.      0.000      0.000

MX      14408771.       712.876      16787074.      10.      14000000.      1.029      14408771.      1.000      1.000

SM     140086256.      6971.005     163878080.      88.     175000000.     19.510     179588720.     14.130     19.000

AV       2918464.       145.229       3414127.       2.       3645833.      0.406       3741432.      0.294      0.396

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  PDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

PLANT-HOUR-REP   = HOURLY-REPORT                                                                                     PAGE  2 -  2

---------------------------------------------------------------------------------------------------------------------------------

CTANK-ST       CTANK-ST      CTANK-ST       CTANK-ST       CTANK-ST       CTANK-ST     CTANK-ST     CTANK-ST

ORAGE          ORAGE         ORAGE          ORAGE          ORAGE          ORAGE        ORAGE        ORAGE

ENERGY         ELECTRIC      ENERGY         CAPACITY       ENERGY         ENERGY       TANK         TOTAL IN

RELEASED       USE           STORED         RUNNING        AVAILABL       REQUESTD     TEMP         STORAGE

BTU/HR         KW            BTU/HR         BTU/HR         BTU/HR         BTU/HR       F            BTU/HR

----( 1)       ----( 3)      ----( 4)       ----( 7)       ----( 8)       ----( 9)     ----(11)     ----(14)

7 1 1             0.        20.000       7196652.             0.      12000000.       8160001.      29.51      77954176.

7 1 2             0.        20.000       7196650.             0.      12000000.       8160001.      29.28      85150848.

7 1 3             0.        20.000       7200480.             0.      12000000.       8160001.      29.05      92347520.

7 1 4             0.        20.000       7200477.             0.      12000000.       8160001.      28.82      99547968.

7 1 5             0.        20.000       7201966.             0.      12000000.       8160001.      28.59     106748416.

7 1 6             0.        20.000        690656.             0.      12000000.       8160001.      28.36     113950400.

7 1 7             0.        20.000             0.             0.      12000000.             0.      28.33     114641024.

7 1 8             0.        20.000             0.             0.      12000000.             0.      28.33     114641024.

7 1 9             0.        20.000             0.             0.      12000000.             0.      28.33     114641024.

7 110             0.        20.000             0.             0.      12000000.             0.      28.33     114641024.

7 111      14400001.        20.000             0.      12000000.      12000000.             0.      28.33     114641024.

7 112      14400001.        20.000             0.      12000000.      12000000.             0.      28.79     100241024.

7 113      14400001.        20.000             0.      12000000.      12000000.             0.      29.25      85841024.

7 114      14400001.        20.000             0.      12000000.      12000000.             0.      29.71      71441024.

7 115      14400001.        20.000             0.      12000000.      12000000.             0.      30.18      57041024.

7 116      14400001.        20.000             0.      12000000.      12000000.             0.      30.64      42641024.

7 117      14400001.        20.000             0.      12000000.      12000000.             0.      31.10      28241024.

7 118             0.        20.000             0.             0.      12000000.             0.      31.56      13841024.

7 119             0.        20.000             0.             0.      12000000.             0.      31.56      13841024.

7 120             0.        20.000             0.             0.      12000000.             0.      31.56      13841024.

7 121             0.        20.000             0.             0.      12000000.             0.      31.56      13841024.

7 122             0.        20.000             0.             0.      12000000.             0.      31.56      13841024.

7 123             0.        20.000             0.             0.      12000000.             0.      31.56      13841024.

7 124             0.        20.000       7158198.             0.      12000000.       8160001.      31.56      13841024.

DAILY SUMMARY (JUL  1)

MN             0.        20.000             0.             0.      12000000.             0.      28.33      13841024.

MX      14400001.        20.000       7201966.      12000000.      12000000.       8160001.      31.56     114641024.

SM     100800008.       480.000      43845080.      84000000.     288000000.      57120004.     715.82    1631237760.

AV       4200000.        20.000       1826878.       3500000.      12000000.       2380000.      29.83      67968240.

MONTHLY SUMMARY (JUL)

MN             0.        20.000             0.             0.      12000000.             0.      28.33      13841024.

MX      14400001.        20.000       7201966.      12000000.      12000000.       8160001.      31.56     114641024.

SM     100800008.       480.000      43845080.      84000000.     288000000.      57120004.     715.82    1631237760.

AV       4200000.        20.000       1826878.       3500000.      12000000.       2380000.      29.83      67968240.

YEARLY SUMMARY

MN             0.        20.000             0.             0.             0.             0.      28.33             0.

MX      14400001.        20.000       7201966.      12000000.      12000000.       8160001.      32.00     114641024.

SM     100800008.       960.000      43845080.      84000000.     288000000.      57120004.    1483.82    1631237760.

AV       2100000.        20.000        913439.       1750000.       6000000.       1190000.      30.91      33984120.

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  EDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- ES-E  SUMMARY OF UTILITY-RATE:  ELEC-ENERGY

---------------------------------------------------------------------------------------------------------------------------------

UTILITY-RATE:  ELEC-ENERGY             RESOURCE:  ELECTRICITY         DEMAND-WINDOW:  HOUR                     3413. BTU/KWH

METERS:  1 2 3 4 5             BILLING-DAY:  31                RATE-LIMITATION:   0.0000

POWER-FACTOR:  0.80             EXCESS-KVAR-FRAC:  0.30              EXCESS-KVAR-CHG:   0.0000

RATE-QUALIFICATIONS                    BLOCK-CHARGES                              DEMAND-RATCHETS        MIN-MON-RATCHETS

--------------------------------       ------------------------------------       ----------------       ----------------

MIN-ENERGY:         0.0              SMMR-DMND-PEAK

MAX-ENERGY:         0.0              SMMR-DMND-SHLDR

MIN-DEMAND:         0.0              SMMR-DMND-OFFPK

MAX-DEMAND:         0.0              WNTR-DMND-PEAK

QUALIFY-RATE:  ALL-MONTHS              WNTR-DMND-SHLDR

USE-MIN-QUAL:          NO              WNTR-DMND-OFFPK

METERED   BILLING   METERED   BILLING   ENERGY   DEMAND   ENERGY                      FIXED  MINIMUM  VIRTUAL    TOTAL

ENERGY    ENERGY    DEMAND    DEMAND   CHARGE   CHARGE  CST ADJ    TAXES  SURCHRG   CHARGE   CHARGE     RATE   CHARGE

MONTH  KWH       KWH       KW        KW           ($)      ($)      ($)      ($)      ($)      ($)      ($)   ($/UNIT)    ($)

-----  --------  --------  --------  --------  -------  -------  -------  -------  -------  -------  -------  -------  -------

JAN     542285    542285    2041.5    2041.5    39823    17630        0        0        0       50        0   0.1060    57503

FEB     478090    478090    2090.5    2090.5    35159    17148        0        0        0       50        0   0.1095    52357

MAR     563646    563646    2138.3    2138.3    41690    17846        0        0        0       50        0   0.1057    59587

APR     550357    550357    2116.9    2116.9    39791    18482        0        0        0       50        0   0.1060    58323

MAY     581971    581971    2548.0    2548.0    40444    38921        0        0        0       50        0   0.1365    79416

JUN     698984    698984    2677.4    2677.4    47502    48579        0        0        0       50        0   0.1375    96131

JUL     682483    682483    2719.7    2719.7    46509    49660        0        0        0       50        0   0.1410    96219

AUG     768954    768954    2866.5    2866.5    52603    49799        0        0        0       50        0   0.1332   102453

SEP     649540    649540    2658.7    2658.7    44169    48505        0        0        0       50        0   0.1428    92723

OCT     566308    566308    2419.2    2419.2    39406    38932        0        0        0       50        0   0.1384    78388

NOV     531117    531117    2194.5    2194.5    39261    18298        0        0        0       50        0   0.1085    57609

DEC     551063    551063    2180.6    2180.6    40455    18816        0        0        0       50        0   0.1076    59321

========  ========  ========            =======  =======  =======  =======  =======  =======           =======  =======

TOTAL   7164798   7164798    2866.5             506812   382617        0        0        0      600            0.1242   890029

T2: Offc Bldg Chicago, 20 Fls, 160x160  50% Sngl Glass U=1.11, SC=1.00, T=1.00   DOE-2.1E-131   8/01/2002    16:04:09  EDL RUN  1

No Day-Lghtg, Wall-U=0.20, Roof-U=0.15  Occ=1P/100sf Lgt=2.0 W/sf Eqp=1.0 W/sf  Systm=PIU, CNTRF-ICESTR, Gas-HW-Boilrs

REPORT- ES-E  SUMMARY OF UTILITY-RATE:  GAS-ENERGY

---------------------------------------------------------------------------------------------------------------------------------

UTILITY-RATE:  GAS-ENERGY              RESOURCE:  NATURAL-GAS         DEMAND-WINDOW:  HOUR                   100000. BTU/THERM

METERS:  1 2 3 4 5             BILLING-DAY:  31                RATE-LIMITATION:   0.0000

RATE-QUALIFICATIONS                    BLOCK-CHARGES                              DEMAND-RATCHETS        MIN-MON-RATCHETS

--------------------------------       ------------------------------------       ----------------       ----------------

MIN-ENERGY:         0.0              WNTR-GAS-ENER

MAX-ENERGY:         0.0              SMMR-GAS-ENER

MIN-DEMAND:         0.0

MAX-DEMAND:         0.0

QUALIFY-RATE:  ALL-MONTHS

USE-MIN-QUAL:          NO

METERED   BILLING   METERED   BILLING   ENERGY   DEMAND   ENERGY                      FIXED  MINIMUM  VIRTUAL    TOTAL

ENERGY    ENERGY    DEMAND    DEMAND   CHARGE   CHARGE  CST ADJ    TAXES  SURCHRG   CHARGE   CHARGE     RATE   CHARGE

MONTH  THERM     THERM     THERMS/H  THERMS/H     ($)      ($)      ($)      ($)      ($)      ($)      ($)   ($/UNIT)    ($)

-----  --------  --------  --------  --------  -------  -------  -------  -------  -------  -------  -------  -------  -------

JAN      31531     31531     257.2     257.2    12925        0        0        0        0        0        0   0.4099    12925

FEB      24633     24633     230.4     230.4    10230        0        0        0        0        0        0   0.4153    10230

MAR      25162     25162     197.1     197.1    10437        0        0        0        0        0        0   0.4148    10437

APR      15408     15408     123.5     123.5     6627        0        0        0        0        0        0   0.4301     6627

MAY       8596      8596     113.4     113.4     3530        0        0        0        0        0        0   0.4106     3530

JUN       1148      1148      87.4      87.4      545        0        0        0        0        0        0   0.4741      545

JUL        665       665      47.7      47.7      315        0        0        0        0        0        0   0.4741      315

AUG        930       930      58.2      58.2      441        0        0        0        0        0        0   0.4741      441

SEP       2343      2343      83.7      83.7     1111        0        0        0        0        0        0   0.4741     1111

OCT       7022      7022      95.8      95.8     2970        0        0        0        0        0        0   0.4230     2970

NOV      16499     16499     179.7     179.7     7053        0        0        0        0        0        0   0.4275     7053

DEC      27924     27924     255.9     255.9    11515        0        0        0        0        0        0   0.4124    11515

========  ========  ========            =======  =======  =======  =======  =======  =======           =======  =======

TOTAL    161861    161861     257.2              67699        0        0        0        0        0            0.4183    67699